## Slide 1: A Proposed Standard for Entity Attestation Laurence Lundblade July 2018

## Slide 2
Bad Devices
Cloned
Tampered
Rooted
Emulating
Real Device
Banking risk engine
IoT backend
Network infrastructure
Enterprise auth risk engine
Electric company
Car components
Good Devices
Entity
Attestation
Token
Chip & device manufacturer
Device ID (e.g. serial number)
Boot state, debug state…
Firmware, OS & app names and versions
Geographic location
Measurement,rooting & malware detection…
All Are Optional
Cryptographically secured by signing

## Slide 3: End-End Attestation Flow
Other flows are possible where verification is done by a service or by the entity vendor.
Entity Manufacturer
(e.g. chip or device vendor)
Entity (e.g., Chip, Device…)
Relying Party (e.g., Server / Service)
EAT Token
Verification Process
Provision private keys during manufacturing
Self-secured token carried in protocol messages
Verification Keys
Processing such as a payment or authentication risk engine
Verified claims
Private key for signing. Stored securely on device
Token Creation and Signing
Claims data

## Slide 4
Four Aspects of Standardization
1. General Structuring and Representation of Claims Labeling of claims Optionality of claims Flexible data representation – integers, strings, binary…
2. Meaning of Individual Claims Interoperability between devices and servers from different vendors
3. Signing Format Accommodate different schemes and algorithms
4. Encryption Format (optional) Accommodate different algorithms
Entity Attestation Token
Claim 1: value
Claim 2: value
Claim 3: value
…
Cryptographically secured by signing
Optional Encryption

## Slide 5: EAT Format
Overall structure: COSE_Sign1
Key ID -- identifies the key needed to verify signature
Certs (optional) -- to chain up to a root for some signing schemes
signature -- Examples: 64 byte ECDSA signature, 256 byte RSA signature
CBOR formatted map of claims that describe device and its disposition
Few and simple or many, complex, nested…
All claims are optional -- no minimal set
The format and meaning of a basic set of claims should be standardized for interoperability
Should be adaptable to cover many different use cases from tiny IoT devices to complex mobile phones
Privacy issues must be taken into account
Algorithm -- Examples: ECDSA 256, RSA 2048, ECDAA
Signing Scheme -- Examples: IEEE IDevID, EPID, X.509 Hierarchy
Signed payload
sig
protected
headers
unprotected
headers
Signature proves device and claims (critical)
Accommodate different end-end signing schemes because of device manufacturing issues
Privacy requirements also drive variance in signing schemes
COSE format for signing
Small message size for IoT
Allows for varying signing algorithms, carries headers, sets overall format
CBOR format for claims
Small message size for IoT
Labelling of claims
Very flexible data types for all kinds of different claims.
Translates to JSON

## Slide 6: Standardization / Extensibility of Claims
Base standard describes how claims work and are formatted in general and
  May include the most common, best agreed upon claims
No claims will be mandatory in base standard
  Verifiers can reject tokens missing claims required in specific use cases
  Profile with minimum sets of claims can be defined, by industry / use case (automotive, power meter…)
Non-standard and proprietary claims will be allowed
  Verifiers can ignore claims they do not understand
The bulk of standardization work will be defining claims well
  Standardized meaning will allow verifiers to interpret claims from devices from different vendors
  This will not always work perfectly and the meaning of some claims may be subjective
IANA (Internet Assigned Names and Numbers) can be used to register claims to avoid collisions and duplications. Similar registries already exist (e.g. CWT and JWT registries).
CBOR itself is extensible for new data types.

## Slide 7: Example Token
[
/ protected / << {
/ alg / 1: -7 / ECDSA 256 /
} >>,
/ unprotected / {
/ kid / 4: h'4173796d6d65747269634543445341323536’
},
/ payload / << {
/ UEID / 8: h'5427c1ff28d23fbad1f29c4c7c6a55’,
/ secure boot enabled / 13: true
/ debug disabled / 15: true
/ integrity / -81000: {
/ status / -81001: true
/ timestamp / 21: 1444064944,
},
/ location / 18: {
/ lat / 19: 32.9024843386,
/ long / 20: -117.192956976
},
} >>,
/ signature / h'5427c1ff28d23fbad1f29c4c7c6a555e601d6fa29f9179bc3d7438bacaca5acd08c8
d4d4f96131680c429a01f85951ecee743a52b9b63632c57209120e1c9e30'
]
Payload Translated to JSON
Integer labels mapped to strings
Binary data base 64 encoded
Floating point numbers turned into strings
{
“UEID” : “k8if9d98Mk979077L38Uw34kKFRHJgd18f==”,
“secureBoot” : true,
“debugDisable” : true,
“integrity”: {
“status”: true,
“timestamp”: “2015-10-5T05:09:04Z”,
},
“location”: {
“lat”: “32.9024843386”,
“long”: “-117.192956976”,
},
}
CBOR diagnostic representation of binary data of full signed token
COSE binary ~130 bytes including sig
JSON text ~500 bytes including a JOSE sig
COSE ECDSA signing overhead is about 87 bytes: 23 for headers and structure, 64 bytes for ECDSA sig

## Slide 8: Device and Submodules
A top-level token is associated with a device – a finished commercial end product
A device may have a set of submodules
      Examples: WiFi subsystem, DSP subsystem
      A submodule has a set of claims of its own
      One level of submodules – keep it simple
      The security of a submodule is either the same or less than that of the device
Tokens may be nested
  This allows submodules that have attestation keys to create their own attestations

## Slide 9: COSE Signing Scheme Flexibility
Many standard algorithms already supported
      RSA, ECDSA and Edwards-Curve Signing (public key)
      HMAC and AES-based MACs (symmetric key)
Extensible for future algorithms
      IANA registry for algorithms exists today
Extensible for special case schemes
      Proprietary simple HMACs schemes, perhaps HW based
      Possibly Intel EPID
      (non-standard algorithms will of course be less interoperable)

## Slide 10: Privacy
Entity Attestation Tokens are intended for many use cases with varying privacy requirements
      Some will be simple with only 2 or 3 claims, others may have 100 claims
      Simple, single-use IoT devices, have fewer privacy issues and may be able to include claims that complex devices like Android phones cannot
Options for handling privacy
      Omit privacy-violating claims
      Redesign claims especially to work with privacy regulation
      Obtain user permission to include claims that would otherwise be privacy-violating
Some signing schemes will be privacy-preserving (e.g. group key, ECDAA) and some will not

## Slide 11: Similar and Related Technologies
Technology | Use Case
FIDO Attestation | Attestation of FIDO Authenticator implementations
Android Key Store | Attestation key pairs in the key store
NEA | Collect and send endpoint security posture (e.g. anti-virus SW state and config) to enterprise collection / monitoring point
RATS / NSF | Attestation / Measurement of SW on Network Security Functions (e.g., firewalls)
TPM | Attestation / Measurement of SW running on a device
BRSKI / Zero Touch | Authenticates IoT devices for enrollment in IoT management system

## Slide 12: More Info
Non-WG mailing list: eat@ietf.org
Mail list info: https://www.ietf.org/mailman/listinfo/EAT
Draft document: https://tools.ietf.org/html/draft-mandyam-eat-00
Github: https://github.com/eat-ietf-wg

## Slide 13: Extra Slides Follow

## Slide 14: Encryption Format
COSE allows for signed data to be encrypted, vice versa (and even countersigning)
CBOR encryption provides algorithm flexibility, structuring and so-on like it does for signing.
Specifies how to combine AES symmetric encryption with EC or RSA public key
Encryption of tokens is optional, but useful
  Protect data that needs to be secret
  Useful in implementing a privacy proxy
  Monetization of an attestation service

## Slide 15: End-end Attestation Flow – Two scenarios
Device / Chip Vendor
Device / Chip
Relying Party
Verification Process
Token
Token
1. Device / Chip Vendor Provides a Service
Provisions private keys during manufacturing
Token – Carried in protocol messages
Token – Sent for verification
Verified payload
Device / Chip Vendor
Device / Chip
Relying Party
Token
Verification Process
2. Device / Chip Vendor Provides Keys
Provisions private keys during manufacturing
Token – Carried in protocol messages
Verification Keys
Verified payload

## Slide 16: Signing Format
COSE (CBOR Object Signing and Encryption) RFC 8152
COSE is an IoT-oriented format for signing and/or encrypting a payload. It is similar to, but much simpler and more compact than PKCS #7, CMS and JOSE
COSE_Sign1: a CBOR array of four
Key id : d25a91aef0b0117e2af9a291 aa32e14ab834dc56ed2a223444547e01
bstr – 64 bytes of ECDSA signature
CBOR formatted map of claims
Maybe small and simple or large, nested and complex
Algorithm : ECDSA 256
payload
sig
protected
headers
unprotected
headers
COSE signed tokens are small, self-secured data blobs that can be embedded in other protocols or written to disk…
COSE provides structuring of payload (to-be-signed data), algorithm identification, key identification and signature
Standard format allows use and development of standard / open source tools

## Slide 17: General Structure & Representation of Claims
CBOR (Concise Binary Object Representation) RFC 7049
  Integers, text, binary, floating point numbers…
  Aggregate types: arrays, maps of label-value pairs
  Reasonably mature – On IETF Standards Track, RFC 7049 published in 2013
  Open source implementations and tools available in many languages at http://cbor.io
  Translatable to JSON by common tools
  Compact code and data for IoT
  Meets goal:
    Top-level of token payload is a CBOR map of label-value pairs
    CBOR maps easily allow for optional data
    CBOR data types are simple & powerful – a top-level claim can be a simple integer or have a complex internal structure